## Slide 1: I/O Systems
Lecture – #31 [16-Apr-2018]
Dept. - CSE 6th Sem
Lecturer: Biswajita Dutta
TA: Akshay Anand
St. Thomas’ College of Engineering & Technology
B. Tech. 6th Semester
Operating System [CS - 603]

## Slide 2: WHY STUDY I/O?
Main jobs of computer:
  I/O
  Processing
In most cases any processing is done by computers in response to some interaction by user through I/O.
60% of codes in Linux have something to do with I/O.

## Slide 3: I/O: Importance

## Slide 4: Previous year MAKAUT questions
Differentiate b/w blocking and non-blocking I/O [2013(IT)]
What are the advantages and disadvantages of linked file allocation technique? How does indexed file allocation technique overcomes the above disadvantages? [2013(CS) ,2017(IT)]
MCQs
Disk I/O generally done in terms of [2013]
a)sector b)bytes c)blocks d)bits

## Slide 5: Basics
I/O devices can be roughly categorized as:
  storage
  communications
  user-interface
  and others
Role of computer I/O : Manage and control I/O operations and I/O devices

## Slide 6: I/O: Elements
Ports
Bus
Controller
Protocols
Interface
Host
Device

## Slide 7: Ports
Devices connect with the computer via ports, e.g. a serial or parallel port.
It is the connection point.

## Slide 8: Bus
A common set of wires connecting multiple devices is termed a bus.

## Slide 9: Controller (I/O processor)
A device controller is a part of a computer system that makes sense of the signals going to, and coming from the CPU.

## Slide 10: Interface
An interface device (IDF) is a hardware component or system of components that provides abstraction for human beings to interact with a computer, a telephone system, or other electronic information system.

## Slide 11: PCI ( Peripheral Component Interconnect )
Used as standard system bus -> for high speed, high bandwidth
Expansion slot -> connects slower low-bandwidth devices, which typically deliver data one character at a time ( with buffering. )
Can connect PCI cards that include:
  Network cards
  Sound cards
  Modems
  Extra ports such as USB or serial
  TV tuner cards
  Disk controllers
  Graphics cards

## Slide 12: PCI ( Peripheral Component Interconnect )

## Slide 13: PCIe ( PCI Express)

## Slide 14: Modern storage options on PCIe
NVMe Flash SSD
NVMe M.2 SSD

## Slide 15: Storage I/O interfaces
Parallel
  SCSI
  ATA/IDE
Serial
  SAS (Serial Attached SCSI)
  SATA

## Slide 16: ATA/IDE – Advanced Technology Attachment

## Slide 17: SCSI – Small Computer System Interface

## Slide 18: SATA – Serial Advanced Technology Attachment

## Slide 20: Daisy chaining
A daisy-chain bus is when a string of devices is connected to each other like beads on a chain, and only one of the devices is directly connected to the host.

## Slide 21: PC Bus Structure

## Slide 22: Port registers
One way of communicating with devices is through registers associated with each port. Registers may be one to four bytes in size, and may typically include ( a subset of ) the following four:
The data-in register is read by the host to get input from the device.
The data-out register is written by the host to send output.
The status register has bits read by the host to ascertain the status of the device, such as idle, ready for input, busy, error, transaction complete, etc.
The control register has bits written by the host to issue commands or to change settings of the device such as parity checking, word length, or full- versus half-duplex operation.

## Slide 23: Memory mapped I/O vs Peripheral mapped I/O
MMIO | PIO
Data is transferred between any general-purpose register and I/O port. | Data is transferred only between accumulator and I/O port.
Easier to use from programmer’s perspective as existing memory instructions can be used for I/O operations along with general purpose registers. | Harder for programmer as extra I/O instructions need to be used, all of which take single operand (means only accumulator can be used).
The memory map is shared between I/O device and system memory. | The I/O map is independent of the memory map.
More hardware is required to decode address. | Less hardware is required to decode smaller I/O port specific address.
Arithmetic or logical operations can be directly performed with I/O data. | Not the case here

## Slide 24: Memory-mapped I/O (MMIO)

## Slide 25: Memory-mapped I/O (MMIO)

## Slide 26: Memory-mapped I/O (MMIO)

## Slide 27: Device I/O port locations on PCs

## Slide 28: I/O or Peripheral-mapped I/O (PIO)

## Slide 29: I/O or Peripheral-mapped I/O (PIO)

## Slide 30: Polling
Polling can be very fast and efficient, if both the device and the controller are fast and if there is significant data to transfer. It becomes inefficient, however, if the host must wait a long time in the busy loop waiting for the device, or if frequent checks need to be made for data that is infrequently there.